CS 245 Assembly Language Programming

Floating Point Arithmetic

Text: Computer Organization and Design, 4th Ed., D A Patterson, J L Hennessy

Sections 3.5-3.8, Pages B.73-B.80

Objectives:  The Student shall be able to:

Convert a fraction to normalized form

Convert a decimal fraction to a binary point form and vice versa.

Perform addition and multiplication with floating point numbers

Convert a fraction to IEEE 754 float or double form (given offsets)

Define overflow and underflow, NAN.

Program assembly language using floating point instructions.

Class Time:

Lecture – Binary fractions, addition, mult.	1 hour

Exercise					1 hour

Lecture – Floating Point formats		1 hour

Exercise					1 hour

Lab						½ hour

Total                                                                4.5 hours

## Fractions: Decimal & Binary

Floating Point is used for Reals or Fractions

Binary numbers are translated as:

25 24 23 22 21 20 . 2-1 2-2 2-3 2-4

Which is equivalent to:

25 24 23 22 21 20 . 1/21 1/22 1/23 1/24

Example:

11.011 = 21 + 20 + 1/22 + 1/23

= 2 + 1 + ¼ + 1/8 = 3 3/8

##### Decimal Point (( Binary Point (( Hexadecimal Point

###### Base 2 -> Base 10

Convert 0.12 to Base 10

0.12 = 1 x 2-1 = 1 / 21 = ½ = 0.510

Convert 0.0012 to Base 10

0.0012 = 1 x 2-3 = 1 / 23 = 1 / 8 = 0.125

Convert 0.011 to Base 10

0.0112 = 1 / 22 + 1 / 23 = ¼ + 1/8 = 3/8 = 0.375

###### Base 10->Base 2

To convert from Decimal to Binary the steps are as follows:

Multiply the decimal fraction by 2.

If result >= 1.0

Digit for answer is 1

Fractional part is used for next iteration

Repeat:

Multiply the decimal fraction by 2

If result >= 1.0 …

Example:

Find value for .375

.375 x 2 = .750	=> 0

.750 x 2 = 1.5		=> 1

.5 x 2 = 1.0		=> 1

(No fraction remaining)

Answer = 0.011

Validate answer:

0.011B = 1/22 + 1/23 = ¼ + 1/8 = .25 + .125 = .375

More Examples:

Convert 0.510 to Base 2

0.5 x 2 = 1.0    	=> 1

0 x 2 = 0		=> 0

Answer: 0.510 = 0.12

Convert 0.7510 to Base 2

0.75 x 2 = 1.5		=> 1

0.5 x 2 = 1.0		=> 1

0 x 2 = 0		=> 0

Answer: 0.7510 = 0.112

Convert 0.2AD16 to Base 2 then to Base 10

0.2AD16 = 0.0010 1010 11012

= 2-3 + 2-5 + 2-7 + 2-9 + 2-10 + 2-12

= 0.16723632812510

Convert 0.2AD16 to Base 10

f=0

f=(0+D)/16 = 13/16 = 0.8125

f = (0.8125+A)/16 = 10.8125/16 = 0.67578125

f = (0.67578125+2)/16 = 0.16723633

Answer 0.2AD16 = 0.1672363310

##### Normalized Form

Fraction Notation:

Normalized form = 1 significant digit

| Fraction | Normalized Form |
| --- | --- |
| 254.66 | 2.5466 x 102 |
| 0.0003 | 3.0 x 10-4 |
| 0.00254 | 2.54 x 10-3 |

To convert to normalized form:

When decimal point does not move, multiply by 100 (=1)

When decimal point moves left 1, add 1 to exponent

When decimal point moves right 1, subtract one from exponent

Example:

1000000000B = 1000000000B*20

1000000000B = 100000000B*21

1000000000B = 1*29

Example 2:

0.0001B = 0.0001B*20

0.0001B = 0.001B*1/2 = 0.001B*2-1

0.0001B = 1.0B*2-4

Binary Point Normalized Notation

25610	=   100000000B	=   1 x 28

810	=   1000B		=   1 x 23

210	=   10B			=   1 x 21

0.510	=   0.1B		=   1 x 2-1

0.7510	=   0.11B		=   1.1 x 2-1

##### Addition

Example:  Add 99.9910 + 0.161010

99.99 = 9.999 x 101

0.1610 = 1.610 x 10-1

To add the two numbers, we must convert first to the larger magnitude: 101

1.610 x 10-1 = 0.01610x101

Now we can add the fractions: 9.999 + 0.01610 = 10.01510

Result: 10.01510 x 101

Round (assuming 4 fractional digits):  10.02 x 101

Renormalize: 1.002 x 102

Example:  Add in binary: 0.510 + -0.437510

0.510 = 1/2 = 1/21 = 0.1B = 1.0 x 2-1

-0.437510 = -7/16 = -7/24 = -.0111B = -1.11 x 2-2

Convert to the larger magnitude: 2-1

1.0 + -0.111 = 0.001

Result:  0.001 x 2-1 = 1 x 2-4 = 1/24 = 1/16 = 0.0625

##### Multiplication:

Multiply 5 x 103 by 3 x 10-2

Without exponents: 5000 x .03 = 150.00

With exponents:

Multiply fractions: 5 x 3 = 15

Add exponents: 3 – 2 = 1

Result: 15 x 101 = 150

## Floating Point Formats

Floating Point Format in Computer:

Example = -25 x 232 => Format = (Sign) (Fraction) x 2(Exponent)

Float = 32 bits

| Sign (1 Bit) 1=negative | Exponent (8 bits) | Fraction (23 bits) |
| --- | --- | --- |

Numbers range between 2x10-38 to 2x1038

Double = 64 bits

| Sign (1 Bit) 1=negative | Exponent (11 bits) | Fraction (52 bit fraction) |
| --- | --- | --- |

Numbers range between 2x10-308 to 2x10308

Reduce the number of Binary Digits

In normalized form each FRACTION is in the form:  1.ffff x 2eeee

To get one additional bit of accuracy it is possible to ASSUME the 1. part above.

Thus the FRACTION part contains ‘.ffff’

When reconstructing the number, you must add: 1 + .ffff to get the original: 1.ffff

##### Comparisons

To compare two numbers

The exponent = magnitude and comes before the fraction.  Therefore…

Comparisons should be easy:  numbers with larger exponents > numbers with smaller exponents

However…

Fractions normally use negative exponents: e.g. 11101010

Large integers use positive exponents: e.g., 00001010

When comparing two numbers:   11101010 > 00001010

Solution:  Bias each float exponent by 127:  EXPONENT = eeee + 127

Solution:  Bias each double-precision exponent by 1023.

When reconstructing the original: eeee = EXPONENT - 127

Most negative exponent=00000000B

Most positive exponent=11111111B

When comparing two numbers:

First compare sign bit: 0 > 1    // positives > negatives

Next compare exponent || fraction:  larger numbers > smaller numbers

##### Example:  Creating an IEEE floating point number

Assume 50.010 = 110010B = 1.10010 x 25

exponent=5	fraction=10010	sign=0

Sign=0  (positive)

Exponent = exponent + 12710 = 101B + 1111111B = 10000100B

Or (in decimal) 5 + 127 = 132 = 10000100B

Fraction = 100100000…

Number = 0…100,0010,0…100,1000,0000,0000,0000,0000 = 0x42480000

Now lets convert back to make sure we did it correctly:

0…100,0010,0…100,1000,0000,0000,0000,0000

Sign = 0 = positive

Exponent = 10000100 - 1111111 = 101 = 5

Or (in decimal) 132 – 127 = 5

Fraction = 0.10010 + 1.0 = 1.10010

Number = 1.10010x25 = 110010 = 32 + 16 + 2 = 50!

Correct!

##### Problems:

Overflow:  Exponent on math operation becomes too large to represent number

- E.g., Multiply by 2 (or -2) in infinite loop => +∞, -∞

Underflow:  Exponent on math operation becomes too small to represent number

- E.g., Divide by 2 in infinite loop => 0

When an invalid operation occurs

NaN: Not a Number = operations using infinity, divide by 0

Exponent value is set to 255.

## Floating Point Instructions

Floating-point coprocessor = coprocessor 1

32 floating point registers: $f0-$f31

Each register is 32 bits

Doubles require 2 registers: specify even register

##### Instructions:

Load/Store			# addr = address in data section, $f = float register

lwc1 	$fdest, addr		# load single from addr containing integer (load word coproc 1)

l.s	$fdest, addr		# load single from addr containing single = lwc1

l.d	$fdest, addr		# load double from addr containing double

mov.d	$fdest, $fsrc		# fdest = fsrc

mov.s	$fdest, $fsrc		# fdest = fsrc

mfc1	$dest, $fsrc		# Move from Coproc. 1: CPUdest = fsrc

mfc1.d	$dest, $fsrc		# CPUdest || CPUdest+1 = fsrc||fsrc+1  // move double

mtc1	$rsrc,$fdest		# fdest = rsrc

s.d	$fsrc, address		# store double from fsrc in fractional form

s.s	$fsrc, address		# store single from fsrc

swc1	$fsrc, address		# store word from fsrc

sdc1	$fsrc, address		# store double word from fsrc // where fsrc = even reg.

Arithmetic Operations

add.d	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 + fsrc2  (double)

add.s	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 + fsrc2  (single)

sub.d	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 - fsrc2  (double)

sub.s	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 - fsrc2  (single)

mul.d	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 * fsrc2  (double)

mul.s	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 * fsrc2  (single)

div.d	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 / fsrc2  (double)

div.s	$fdest, $fsrc1, $fsrc2		# fdest = fsrc1 / fsrc2  (single)

neg.d	$fdest, $fsrc			# fdest = -fsrc  (double)

neg.s	$fdest, $fsrc1			# fdest = -fsrc (single)

Other mathematical operations

These are shown with single precision (s) but double precision (d) is also available

abs.s	$fdest, $fsrc			# fdest = |fsrc|

sqrt.s	$fdest, $fsrc			# fdest = root(fsrc)

Conversions

Floating point registers can contain integer formats - you must keep track.  In all cases below, operations can be done either with single or double precision.

cvt.d.s		$fdest, $fsrc		# fdest = (double) fsrc		// single ( double

cvt.s.d		$fdest, $fsrc		# fdest = (single) fsrc		// double ( single

cvt.s.w		$fdest, $fsrc		# fdest = (single) fsrc		// int ( single

cvt.d.w		$fdest, $fsrc		# fdest = (double) fsrc		// int ( double

cvt.w.s		$fdest, $fsrc		# fdest = (single) fsrc		// int ( single

cvt.w.d		$fdest, $fsrc		# fdest = (double) fsrc		// int ( double

ceil.w.s	$fdest, $fsrc		# fdest = (integer rounded up) fsrc

floor.w.d	$fdest, $fsrc		# fdest = (integer rounded down) fsrc

trunc.w.s	$fdest, $fsrc		# fdest = (truncated integer) fsrc

round.w.s	$fdest, $fsrc		# fdest = rount(fsrc)

Comparisons

Eight condition codes (cc) exist, where the flip-flop is set

Replace cc below with a number between 0..7

c.eq.s	cc $fsrc1, $fsrc2		# cc = (fsrc1 == fsrc2)

c.lt.s	cc $fsrc1, $fsrc2		# cc = (fsrc1 <   fsrc2)

c.le.s	cc $fsrc1, $fsrc2		# cc = (fsrc1 <= fsrc2)

bc1f	cc label			# if cc == 0 (false) then branch

bc1t	cc label			# if cc == 1 (true) then branch

movf.d $fdest, $fsrc, cc		# if cc == 1 then $fdest = $fsrc

E.g.,	c.eq.d	0  $f0,$f2		# if $f0==F2 then set cc0 to 1

bc1f 	0  label

Other test conditions: ge, gt, ne, also exist.  Other conditional move instructions exist too.

NOTE: USE CC CODE = 0!  OTHER CC CODES DO NOT WORK WITH XSPIM!

###### System Calls: Reading & Printing

Printing:  Register conventions:

Print float:	$v0=2		$f12=float register to print

Print double:	$v0=3		$f12=double register to print

Reading:  Register conventions:

Read float:	$v0=6		$f0=float is returned in reg $f0

Read double:	$v0=7		$f0=double is returned in reg $f0

Example:			# print (total+count);

li	$v0, 2

add.s	$f12,$f2,$f12

syscall

###### Allocating Data

#				# Creating two variables: tax[0]=0.05; tax[1]=0.06

tax:	.float	0.05, 0.06

#				# Creating double precision variables.

dprec:	.double	0.3552, 0.4422, 13.3232

### Floating Point Example

Thanks Josh!!!

#       Name:           Josh Odom

#       Course:         Cs355

#       Assignment:     1

#       Program:        2

#

#       This program will prompt the user for 5 numbers, and it will average

#	them and display the result.

.data

#				the double constant for 5

five:	.double	5.0

#				the double constant for 0

zero:	.double	0.0

#				a greeting message

greet:	.asciiz	"Enter 5 numbers, and I'll average them for you.\n"

#				the first part of the input display

first:	.asciiz	"Enter "

#				the last part of the input display

last:	.asciiz " number: "

#				the endings for 1, 2, 3, 4, 5

nums:	.asciiz  "st", "nd", "rd", "th", "th"

#				a message for the result

average:.asciiz 	"The average is: "

.text

.globl main

main:

AVG00:

#				save $ra on stack

addi	$sp,$sp,-4

sw	$ra,0($sp)

#				$s0 is the current value, $s1 is 1 past the

#				last value

li	$s0, 0

li	$s1, 5

#				set the running total to 0

ldc1	$f12, zero

#				display greeting

li	$v0, 4

la	$a0, greet

syscall

AVG01:

#				store $s0 in the first argument, and do a call

#				to the print routine

move	$a0, $s0

jal PRT00

#				get a double from the keyboard

li	$v0, 7

syscall

#				add the new double to the running total

add.d	$f12, $f0, $f12

#				increment the counter

addi	$s0, $s0, 1

#				once the counter reaches 5, then break

bne	$s0, $s1, AVG01

#				display a message for the result

li	$v0, 4

la	$a0, average

syscall

#				find the average of the numbers

ldc1	$f0, five

div.d	$f12, $f12, $f0

#				display that average

li	$v0, 3

syscall

#				return the old $ra back to its proper position

lw	$ra,0($sp)

addi	$sp,$sp,4

#				return

jr $ra

PRT00:

addi	$sp,$sp,-4

sw	$ra,0($sp)

#				save $a0 in $t0

move	$t0, $a0

#				display the first part of the input message

li	$v0, 4

la	$a0, first

syscall

#				display which number we're one (one more than

#				the number we got

li	$v0, 1

addi	$a0, $t0, 1

syscall

#				multiply the number we got by three, and that's

#				the offset for the correct number suffix (1st, 2nd, 3rd, …)

mul	$t0, $t0, 3

la	$t1, nums

addu	$a0, $t0, $t1

#				display that number suffix

li	$v0, 4

syscall

#				and display the last part of the input message

li	$v0, 4

la	$a0, last

syscall

#				return

lw	$ra,0($sp)

addi	$sp,$sp,4

jr $ra

### Exercise 1: Working with Binary Point

Convert these decimal numbers to decimal normalized floating point form:

12510 =

0.0034310 =

1101.11B =

0.0101B =

Convert these binary point numbers to Base 10:

(Hint: Determine powers of two:  0.1 = 2-1 = 1/21)

0.112=

0.101012=

Convert this decimal fraction to binary for at least 6 digits (or 6 binary places):

(Hint: Multiply fraction by 2: if quotient > 1 binary digit is one.  Repeat)

0.3310=

Normalize the following decimal numbers to the larger of the two exponents, then add them:

20.5 + 250.25

Now convert the numbers to binary, normalize them, and add them in binary:

Multiply the following two binary numbers:  1.001 x 23 * 1.01 x 22

Then convert the numbers to decimal and check your work.

(Hint:  Multiply the fractions and add exponents)

### Exercise 2:  Working with IEEE-formatted Floats & Doubles

For the following exercise, the following float and double variables were allocated in a MIPS program.

[0x10010000]	0x41f00000  0x3cf5c28f  0x453b8000  0x40400000

[0x10010010]	0x3e99999a  0x43960000  0x3b449ba6  0xc1f00000

[0x10010020]	0xc3960000  0xc53b8000  0xc0400000  0xbe99999a

[0x10010030]	0xbcf5c28f  0xbb449ba6    d=0x00000000  0x403e0000

[0x10010040]	d=0x00000000  0x4072c000  d=0xbc6a7efa  0x3f689374

[0x10010050]	d=0x00000000  0x40080000  d=0x33333333  0x3fd33333

[0x10010060]	d=0xeb851eb8  0x3f9eb851  d=0x00000000  0x40a77000

|  | Float | -Float | Double |
| --- | --- | --- | --- |
| 0.003 |  |  |  |
| 0.03 |  |  |  |
| 0.3 |  |  |  |
| 3 |  |  |  |
| 30 |  |  |  |
| 300 |  |  |  |
| 3000 |  |  |  |

### Java Lab:

Write a java (or c++) program that uses floats to:

Print the number 0.333,333,33

Adds 0.333,333,33 to a total 100,000 times.

Multiplies 0.333,333,33 x 100,000

Compare the sum and the multiplication result.  Do they match?  Why not?  Which one is correct?

Then retest using 10,000,000 (instead of 100,000)

Compare the sum and the multiplication result.  Do they match?  Why not?  Which one is correct?

Then retest using doubles.

What does this teach you about using floats or doubles and summing?  How can this error be avoided?

For hackers only:  How is zero stored in floating point notation?