Cs 355 Computer Architecture

Bus Interfaces

Text: Computer Organization and Design, Patterson & Hennessy

Chapter 6.5-6.6

Objectives:  The Student shall be able to:

Describe the two basic transactions that occur over a bus.

Describe the basic use of the data, address, and control lines for a bus.

Define the difference in operation between synchronous and asynchronous busses.

Define basic definitions: memory-mapped I/O, parallel, serial, hot-pluggable.

Define UMA and NUMA, and draw a configuration of each.

Define the 4 common protocol layers in a point-to-point interconnect, and describe their basic functions.

Define CRC, balanced transmission.

Class Time:

Lecture					1.5 hours

Exercises					1.5 hours

Total                                                                3 hours

# Bus Interfaces

Memory Architecture

UMA: Uniform Memory Access:

E.g.:  All memory is shared on a bus for all processors

NUMA: Non-Uniform Memory Access:  Local memory and remote memory

E.g.: Each processor has its own memory, which is not easily accessible to other processors

### Interconnect Protocols

(These, QPI, and PCIe notes taken from: Computer Organization & Architecture, 9th Ed., William Stallings, Pearson Ed. 2013.)

Modern interfaces work mainly with switches or point-to-point interfaces.

Layered Architecture:

| Transaction | Defines and Exchanges Packets: Command Type: Memory Read (0) / Write (1) E.g., Read=10 I/O Read (0) /Write (1) E.g., Write=21 Configuration: Command requests to I/O devices Message: Error handling, interrupts, power mgmt Completion: Command completed = 50 Sequence Number or Tag: Data: Address, Command, and/or Data |
| --- | --- |
| Routing | Optional: Routes packets through the system Source Address: Where packet is from Destination Address: Where packet is going to |
| Link | Reliable transmission and flow control Cyclic Redundancy Check (CRC): Sophisticated checksum verifies accuracy Flow Control: Permission is given to send N packets. |
| Physical | Electrical interface for transmission and reception: Data Lanes (or lines): Parallel transmission of bits Balanced Transmission: Return circuit: Tx 1 Rx 0; or Tx 0 Rx 1. |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd(2) /Tag(2) | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |

Flow Control:

- At initialization, credits are allocated

- Each ‘flit’ packet transmitted consumes one credit.

- When buffer processed at receiver, a credit is sent back.

Error Control:

- Sender keeps copy of packet until it is acked

- When packet received with CRC error, bit(s) have been mutilated, NAK is returned

QuickPath Interconnect (QPI)

Characteristics include:

- Multiple direct connections:  Each device may interface directly to other devices

- Layered Protocol with packet data transfer

- NUMA example shown above

Physical Layer:

20 data lanes (or lines) in each direction: 1 bit time = 20 bits transmitted

Clock: Transmit in each direction

DataLink:

Flow Control:  Prevents data overflow at receiver

Error Control:  Checks CRC and retransmits on error

Routing:

Supports routing packets through other nodes

QPI Protocol Layer:

Sends data, but supports other features too: e.g., cache coherency

PCIe or Peripheral Component Interconnect Express

Characteristics:

- UMA access shown

Devices include:

Chipset:

- Translates between Core/Memory interface, PCIe interfaces, legacy interface

- Buffers packets to accommodate slower components

Switch: Routes packets to their destination

PCIe Endpoint: E.g., Gigabit Ethernet, video controller, disk interface, comm. controller

Physical layer:

Bidirectional Lanes: 1,4,6,16 or 32 lanes multiplexed data

No transmitted clock can result in clock drift in long strings: 00000000000000000000000

Scrambling: Data randomization avoids long strings of similar bits

Encoding: Additional bits added per fixed size frame to help in synchronization

Parallel to Serial: Transmits one bit at a time

Data Link Layer:

- 16 bit sequence number

- 32-bit CRC

Processing:

- Transmitter: Keep copy of packet until ACK received

- Receiver: Sends NAK if packet received in error

Transaction Layer:

Request/Response protocol: Response => Completion

Some additional fields:

- Length: in Double Words=4 bytes

- Attributes: No Snoop: Cache coherence is not a concern

- Traffic Class: Priority

Exercise: QPI Interconnect Interface

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |

| Framing | Link: Seq. | Routing: Src/Dest | Transaction: Cmd / Tag | Data | Link: CRC | Framing |
| --- | --- | --- | --- | --- | --- | --- |
| 7e |  |  |  |  |  | 7e |
| 0 | fa bc 12 3e 98 f3 f0 b0 a3 a4 b9 87 |
| 1 | 23 98 38 15 a4 b3 cd 00 ff f0 a1 83 |
| 2 | 98 73 3a 8b f0 dc 13 5d a3 89 9f ab |
| 3 | 12 ba 45 dc 94 82 cc a0 fb a9 87 13 |

| 0 | fa bc 12 3e 98 f3 f0 b0 a3 a4 b9 87 |
| --- | --- |
| 1 |  |
| 2 |  |
| 3 |  |

| 0 |  |
| --- | --- |
| 1 | 23 98 38 15 a4 b3 cd 00 ff f0 a1 83 |
| 2 |  |
| 3 |  |

| 0 |  |
| --- | --- |
| 1 |  |
| 2 | 98 73 3a 8b f0 dc 13 5d a3 89 9f ab |
| 3 |  |

| 0 |  |
| --- | --- |
| 1 |  |
| 2 |  |
| 3 | 12 ba 45 dc 94 82 cc a0 fb a9 87 13 |

Core Directions for protocol use:

Link Sequence Number = Tag = 0,1,2 for each Core you send to (keep track)

Routing Src/Dest: Source Core, Dest Core numbers (e.g., 2 1 = from Core 2 to Core 1)

Transaction Cmd: 10=Memory Read, 11=Memory Write

Data: For Cmd=10:

To mem: Address of memory you want to read.  Start with 0000 for byte 0.

From mem: Data sent back.  Assume you can send 4 bytes.

Link CRC:  Number of characters in your packet (very simplistically calculated)

| Core # | Tag & Sequence Number sent: |
| --- | --- |
| Core 0 |  |
| Core 1 |  |
| Core 2 |  |
| Core 3 |  |

PCIe Interconnect Interface Exercise

CORE0:

Write to Memory Address 0000:  fa bc 10 2a 00 34

Wait for a Done reply on each send

Read from Device 1 (with address 10001)

CORE1:

Write to Device 2 (address 10002): a3 2f 39 fb 3d 8a 2d 1c 00

Wait for a Done reply on each send

Read from Memory Address 0004 for 4 bytes

DEVICE 1:

You have received from your device: a1 b2 3f 40

Wait until you receive a read before sending the data in.

Handle one command at a time.

DEVICE 2:

You will receive data, which you must store.

Handle one command at a time.

Send a Completion in response

CHIPSET (1 assigned to each Core):

Data to Core & Memory is in Bus Format

- Example: Address for Device 2 is 10002

Data to Devices is in PCIe format

MEMORY:

Your memory is currently all 0s.

You will receive read and write requests.

You only handle one request at a time.

Send a Done to the CHIPSET as a reply

Bus Format:

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

| Command Read=0 / Write=1 / Done=2 | Address (Top bit: 0=Memory 1=Device) | Data |
| --- | --- | --- |

# Text boxes

I/O Device

I/O Device

I/O Hub

PCIe

PCIe

QPI

DRAM

DRAM

CoreB

CoreA

Memory Bus

QPI

DRAM

CoreD

CoreC

DRAM

QPI

PCIe

PCIe

I/O Device

I/O Device

I/O Hub

Core

Core

Memory

Gigabit

Ethernet

Chipset

Host bridge

PCIe

Memory

PCIe

PCIe

Switch

PCIe

PCIe Endpoint

PCIe Endpoint

PCIe Endpoint

Legacy Endpoint